## PRINTING

Technology: Multi printhead thermal ink jet Printheads: 10 semi-permanent printheads each with 208 nozzles (4 › black, 2 › cyan, 2 › magenta, 2 › yellow) True resolution: 600 › 600 dpi Minimum pen thickness: .0032 inches Calibration: Automatic printhead alignment Failing nozzle compensation Unattended printing in the overnight mode Size of ink tanks: 400 ml Ink level monitoring: Ink level indication Out of ink signaling Margins: Leading and trailing strip: .2 inch Left and right sides: .12 inch Width detection: Automatic Media types: Uncoated (17–24#) Coated (24#) Polyester films (3–4 mil) Alternate photo glossy (50#) Vellum (16–20#) Media Sources: 1 or 2 front loadable rolls Media core size: 2" Maximum roll length: 300 feet Output delivery: Slide, front-accessible Noise level: Less than 44 dB (A) standby Less than 65 dB (A) printing Dimensions: 58" (h) › 77" (w) › 41" (d) Electrical requirements: 100/120/230 Volt 50/60 Hz Power consumption: EPA-sleepmode (printer only)* 38 W Standby 108 W Run 159 W Note: Printer and Océ Power Logic® controller excluding monitor Weight: 364–397 lbs. Safety approvals: CE-compliance, TÜV-GS (IEC60950), UL, Cul (according to standard CAN/CSA C22.2 No 60950), CB Compliance with EN 60950 Other: Energy Star® compliant

## SCANNING

| Technology: |  | Fully integrated RGB color scanning |
| --- | --- | --- |
| Cameras: |  | 3› Reduction type CCD Cameras |
| Optical resolution: |  | 508 dpi |
| Calibration: |  | Automatic color calibration based on IT8.7-card Automatic camera alignment Automatic stitching control |
| Mechanical speed: |  | Max 8 ips |
| Scanning width: |  | Max. 40" / 1016 mm |
| Original thickness: |  | Max. 0.60 inch |
| Original feed: |  | Face down |
| Original out: |  | Rewind and hold Feed and release Feed and hold |
| Original delivery: |  | Slide, front accessible Optional: original delivery rack at the back |
| Dimensions: |  | 42" (h) › 53" (w) › 20" (d) |
| Electrical requirements: |  | 100/120/230 Volt 50/60 Hz |
| Power consumption: |  | Sleepmode: 45 W Stand-by: 135 W Run: 135W |
| Warm up time: |  | From sleep mode: about 6 mi. From cold start (timer controllable) about 6 min. |
| Weight: |  | 232 lbs. |
| Safety approvals: |  | CE Compliance, TÜV-GS (IEC60950), UL, CB compliance with EN60950, EMC Compliance |

## COPYING

| Copy processing technology: |  | Océ Image Logic® Color |
| --- | --- | --- |
| Color management: |  | Based on OMP-profiles |
| Number of copies: |  | 1–99 Set Memory: scan once, process once, print many |
| Original handling: |  | Manual or automatic size detection Automatic Deskewing |
| Job settings: |  | Programmable default setting Pre-programming of the next copy Single sheet or multiple sheet/set Priority setting on job level Start printing while scanning |
| Copy color modes: |  | Grayscale, color, blueprint |
| Copy quality modes: |  | Check, release, presentation Automatic resolution optimization |
| Copy content modes: |  | Text & lines, Area fills |
| Exposure control: |  | Manual fine adjustment Automatic background compensation (on/off ) |
| Copy manipulation: |  | Leading strip adjustment (add or remove up to 16 inches) Invert Image mirroring Positioning Keep or delete region of interest |
| Scale: |  | Manual: 10–1000 % Automatic: fit to media size fit to standard media format |
| Roll/media selection: |  | Manual, Automatic |
| Cut length: |  | Standard, Synchro or user defined |