LT904

Main Features

1.Adopting Dong fang hong famous diesel engine,good reliability、large torque reserve、low fuel consumption, high economic benefits;

2.Operate independently double clutch ，high transfer ability、reliable effect、operation more comfortable;

3.Gear box use 4X(4+2),16 forward gears,8 reverse gears, gear are reasonable,high working efficiency;

4.Adopt independent power output device,steady transmission,large bearing capacity;

5.Using independent oil hydraulic steering system operation,flexible operation,reliable energy saving;

6.Using disc brakes,large braking torque,good braking effecting;

7.Using forced type lifter, reliable use, convenient maintenance;

8.Final drive adopts planetary reduction structure,compact structure, large reduction ratio;

9.New streamlined appearance, greaceful ,HY,fashion;

Main technical parameters

| model | LT904 |
| --- | --- |
| type | 4X4 |
| Overall dimension(mm) | Length | 4396 |
|  | Width | 2038 |
|  | High | 2810 |
| wheelbase(mm) | 2195 |
| Front wheel tread(mm) | 1610 |
| Rear wheel tread(mm) | 1620-2020 |
| Min.turning radius(m) | One side brake | 4.2±0.3 |
|  | One side not brake | 4.9±0.3 |
| Min.using mass | 4090 |
| Gear box | F16/R8 |
| Speed(km/h) | going | 1.58-33.69 |
|  | retread | 2.41-34.67 |
| Engine | model | LR4M5-23 |
|  | Rated power(kw) | 66.2 |
|  | Rated speed(r/min) | 2300 |
| Tyre type | Front tyre | 11.2-24 |
|  | Rear tyre | 16.9-34 |
| Steering system type | All hydraulic front wheel steering |
| Max.lift-off weight(KN) | 15.9 |
| PTO type | Rear-mounted semi-detached |
| PTO speed(r/min) | 760/1000(540/1000 or 540/760 or 760/850 is also available) |
| PTO power(kw) | 56.3 |
| Roots in control mode | Height adjustment,floating control |
| Max.traction(KN) | 21.3 |
| Counterweight quality(kg) | front | 270 |
|  | rear | 470 |