DEBITMETRE INDUSTRIALE LICHIDE USOR VISCOASE -NORMALE –CHIMIC AGRESIVE

Excellent stepless adjusting me chanism allows a micro adjustment of the meter High accuracy and repeatability over the widest range of flow; Superior accuracy at constant flow Low maintenance, no metal-to-metal contact in measuring chamber, long life service Low pressure loss, a true gravity flow meter Accuracy regardless of pressure fluctuations, temperature variation, viscosity Choice of aluminum, cast iron and stainless steel materials of construction. Industries Automotive; Adhesives; Agriculture; Asphalt ; Aviation fueling ; Animal feeds; Beverage; Cosmetics ; Chemical processing; Concrete Add mixtures; Dairy; Liquid fertilizers; Food processing ; Fuel Oil delivery; General industrial; Hydrocarbon processing; Liquefied gases; Lube oils; Marine ; Paint and varnish ; Petroleum marketing ; Petroleum production ; Pharmaceutical; Printing ink; Pulp &paper; Refining commercial Solvents; Recycling ; Railroad ; Textile. Application: Refined petroleum products; Aviation gasolines and jet fuels; A wide variety of products such as: liquid sugars, corn syrup, corn sweetners, dextrose, fructose, sucrose, maltose, lactose, corn oil, soy bean oil, cotton seed oil, coconut oil,. Treated waters (deionized, demineralized, and potable); Chlorinated solvents and general solvent metering; Acid pH liquids; Liquefied petroleum gas(LPG); Crude oil, also for heated and/or viscous liquids; Oil or water based latex products, polyester resins, and adhesives (neutral pH), also for metering herbicides and nitrogen fertilizer solutions; Herbicide; Sodium hydroxide (caustic) solutions, high sulfur crude oil (LACT and NOD) and other alkaline pH liquids Abrasive liquids Model IM-40 IM-50 IM-50 IM-80 IM-80 IM-100 IM-100H IM-150 IM-150 Size 40mm / 1" 50mm / 2 " 80mm / 3 " 100mm / 4 " 150mm / 6 "and 100mm / 4 " for option Flow Range (L/min) 25-250 38-380 55-550 75-750 115-1500 130-1300 170-1700 225-2500 300-3000 Volume Per Revolution 0.309L 0.681L 1.839L 5.102L 9.507L Max.Pressure +-0.2% Accuracy +-0.2% Repeatability +-0.05% Standard Measurement LITER / US Gallon /IMP Gallon Model IM-40 IM-50 IM-80 IM-100 IM-150 Dimension 53¡Á48¡Á53mm 53¡Á48¡Á53mm 58¡Á50¡Á61mm 76¡Á64¡Á72mm 80¡Á65¡Á79mm Net Weight 23kg 26kg 40kg 70kg 130kg Gross eight 35kg 38kg 55kg 90kg 155kg Package 1pc/Wooden Case